VGA has primarily 5 main signals:
- Red
- Green
- Blue
- Hsync : Horizontal Sync
- Vsync : Vertical Sync

One can assign memory in registers for RGB to control how many colors to have on our screen.

PS2 has 2 main signals:
- clock
- data : 11 bit packet (intended data is sampled on falling edge)

When no data is transmitted, both clock and data signals are low.

For including a module from other file in same folder, use syntax

`include “another_file.v”
`include “folder/another_file.v” //for further into a directory